## Slide 2: SUMMARY
CONFIGURATIONS
ERGONOMICS
WORKFLOW
CLINICAL APPLICATIONS

## Slide 3: CONFIGURATIONS
Omniscop DReam
Generator 5 KW – Flat panel 21X21 cm
Generator 5 KW – Flat panel 30X30 cm
Generator 20 KW – Flat panel 21X21 cm
Generator 20 KW – Flat panel 30X30 cm

## Slide 4: CONFIGURATIONS
Generator 5 KW
Monoblock
High frequency 40 kHz
Max voltage 120 kV
5 à 100 mA

## Slide 5: CONFIGURATIONS
Generator 20 KW
Monoblock
High frequency 40 kHz
Max voltage 120 kV
12,5 à 150 mA

## Slide 6: CONFIGURATIONS
Flat panel 21X21
TRIXELL Pixium 2121S
154µm
25 fps
Scintillator Iodide of cesium
DQE : 65% - 0,5 lp/mm
MTF : 80% - 0,5 lp/mm
Matrix 1334 x 1334 pixels

## Slide 7: CONFIGURATIONS
Flat panel 30X30
TRIXELL Pixium 3030S
154µm
25 fps
Scintillator Iodide of cesium
DQE : 65% - 0,5 lp/mm
MTF : 80% - 0,5 lp/mm
Matrix 1954 x 1954 pixels

## Slide 8: ERGONOMICS
C-arm
Depth : 71 cm
SID : 107 cm
Orbital rotation
95°/+65°
Horizontal rotation
+/-200°

## Slide 9: ERGONOMICS
Variable height motorised
+/-45 cm
Swivel
+/-12°

## Slide 10: ERGONOMICS
Visualisation console
Screens rotation +/-180°
Variable height 153 to 178 cm
2 Full screens HD 22 ’’

## Slide 11: ERGONOMICS
Operator screens
Touch interface 12’’
Access to protocols and acquisition parameters
Real-time image display

## Slide 12: ERGONOMICS
Dose management
Removable anti-scattered grid
Virtual collimation

## Slide 13: WORKFLOW
Customizable protocols
Continuous Fluoroscopy / Pulsed / Snapshot
Frame rates : 1 to 25 images/s
Acquisition parameters customizable by protocol (KV, mAs, collimation, Zoom, ...)

## Slide 14: WORKFLOW
Visualisation console
22’’ Full HD screens
2 touch screens (« Reference » image and « live » image)
Storage around 135 000 images

## Slide 15: WORKFLOW
User interface
Customizable protocols
Advanced Post-processing (Recursives et spatials filters)
Annotations (liste and free)
Mesureaments and advanced tools (calculation of stenosis )

## Slide 16: WORKFLOW
Dicom 3.0 options
Worklist
Store
Print
Query/Retrieve
Media export (USB)
Storage commitment
RDSR (structured dose report)
MPPS

## Slide 17: CLINICAL APPLICATIONS
Orthopedics
Hip
Extremities
….

## Slide 18: CLINICAL APPLICATIONS
Neurosurgery
Skull
Spine

## Slide 19: CLINICAL APPLICATIONS
Thorax /Abdomen
Pacemaker
Cholangiography
…

## Slide 20: CLINICAL APPLICATIONS
Peripheral vascular
Abdominal vascular

## Slide 21: CLINICAL APPLICATIONS
Cerebrovascular
Carotids
Aneurism control
Cardiac
Angioplasty
Picc line (pose of chamber for chemotherapy)